## Slide 1
ML Architecture Person Detection
Person detected
NO Person detected

## Slide 2
based on the MobileNets Architecture
split standard convolution into depthwise separable (depthwise+pointwise) convolution
 fewer multiplications, reduces model size and computation time
ML Architecture Person Detection
MobileNets: Efficient Convolutional Neural Networks for Mobile Vision Applications, A. G. Howard et al., 2017

## Slide 3
Depthwise separable Convolution
=
+
Convolution
Depthwise Convolution
Pointwise Convolution
https://eli.thegreenplace.net/2018/depthwise-separable-convolutions-for-machine-learning/

## Slide 4
ML Architecture Person Detection
INPUT ([1,96,96,1])
DepthwiseConv
DepthwiseConv
PointwiseConv
repeat this layer structure 13x (different weight/input dimensions)
PointwiseConv
AvgPool
Softmax
OUTPUT ([1,2])
INPUT: grayscale int8 image (96x96 pixels)
OUTPUT(1x2 vector indicating probability for Person/No Person label)
int8-Model, model also makes use of quantization (therefore int32 and int64 values in quant layers)
 rather large network, but repetitive architecture
31 Layers in total
Notes: TF Lite File 300kB in size

## Slide 5
ML Architecture Person Detection
INPUT ([1,96,96,1])
DepthwiseConv
DepthwiseConv
PointwiseConv
repeat this layer structure 13x (different weight/input dimensions)
PointwiseConv
AvgPool
Softmax
OUTPUT ([1,2])
31 Layers in total
Notes: TF Lite File 300kB in size

## Slide 6
Depthwise Convolution
groups = 1
input
weights
output
sum
Notes: TF Lite File 300kB in size

## Slide 7
Depthwise Convolution, groups = 1
input
weights
output
sum
Notes: TF Lite File 300kB in size

## Slide 8
Depthwise Convolution, groups = 1 for layer 1
1x96x96x1
input
weights
output
1x48x48x8
stride = 2
Notes: TF Lite File 300kB in size

## Slide 9
Depthwise Convolution, groups = channels
1xHxWxC
1xHxW
1xHxW
1xHxW
1xHxW
input
weights
output (stride=1)
1xH/2xW/2
1xH/2xW/2
1xH/2xW/2
output (stride=2)
1xH/2xW/2
Notes: TF Lite File 300kB in size

## Slide 10
Average Pooling
A1
A3
A4
A2
B1
B3
B4
B2
C1
C3
C4
C2
D1
D3
D4
D2
∅A
∅C
∅D
∅B
Notes: TF Lite File 300kB in size

## Slide 11
Softmax
used as last activation function to normalize output to a probability distribution
 scales logits/numbers into probabilities
-128
68
Not a Person
Person
Logits
0.05%
99.95%
Output Probabilities
NN Layer Output
Softmax
Classes
Notes: TF Lite File 300kB in size

## Slide 12
Quantization
int8
0
255
float32
21359.2
-1034.5
Notes: Quantization of weights/bias

## Slide 13
Quantization
Convolution
int32
Multiplication with Quantization parameters
int64
Addition with Quantization parameters
int64
Shifting with Quantization parameters
int8
Notes: Quantization of activation values

## Slide 14
ROADMAP C Implementation Person Detection
Train Model based on the MobileNet with the VWW COCO Dataset with TF
Accuracy: 81.5%
1. Train ML Model
2. Extract parameters from trained model
implement the ML model in native C to allow an acceleration with the HyCube CGRA in the future
3. C implementation of ML Model
4. Deploy model on Manuca
Extract weights, bias and quantization parameters from the trained TFLite model for the C implementation
Run the TFLite and the C model on the Manuca Microcontroller and evaluate computation speed and energy consumption as well as accuracy
in the future the C implementation shall be accelerated with the HyCube CGRA to achieve even faster and more efficient results
5.Acceleration with HyCube CGRA

## Slide 15
Manuca Board
MCU: STM32F767ZI, based on ARM Cortex M7 CPU architecture
2MB Flash
512kB SRAM
Debug via Serial UART interface

## Slide 16
Optimizations done for C Implementation
to minimize SRAM usage:
  make model parameters local, not global
  partition large layers with a lot of parameters into smaller portions (just for layer 27, 256x256 weight dimension)
  work with smaller storage size if applicable (e.g.: int8 instead of int32 for quantization shift param, int16 instead of int32 for bias)
to optimize time per inference
  make model parameters global to minimize flash memory access

## Slide 17
Analysis mbed implementation
Implementation | TFLite | Native C (params are local variables) | Native C (params are global variables)
Time per Inference | 98,7 ms  10.13 fps | 430 ms  2.33 fps | 360 ms  2.78 fps
Power [W] | 0.75 | 0.7 | 0.73
Voltage [V] | 5.08 | 5.08 | 5.08
Current [A] | 0.148 | 0.139 | 0.144
Energy [J] | 0.752 | 0.70612 | 0.732
SRAM usage | 144 kB | 16.4 kB | 202.3 kB
Flash usage | 97.5 kB | 308.1 kB | 303.8 kB
Binary size | 420 kB | 309.6 kB | 284 kB
Notes: TF Lite File 300kB in size

## Slide 18
Analysis mbed implementation
Implementation | TFLite | Native C (params are local variables) | Native C (params are global variables)
Time per Inference | 98.7 ms  10.13 fps | 430 ms  2.33 fps | 360 ms  2.78 fps
Power [W] | 0.75 | 0.7 | 0.73
Energy [J] | 0.752 | 0.70612 | 0.732
SRAM usage | 144 kB | 16.4 kB | 202.3 kB
Flash usage | 97.5 kB | 308.1 kB | 303.8 kB
Binary size | 420 kB | 309.6 kB | 284 kB
fastest implementation
most power efficient
implementation
Notes: TF Lite File 300kB in size

## Slide 19
Analysis mbed TFLite implementation
Notes: TF Lite File 300kB in size

## Slide 20
Analysis mbed native C implementation
parameters as local variables
parameters as global variables
Notes: TF Lite File 300kB in size

## Slide 21
Possible Future Improvements
minimize model size
  use a smaller input size (currently 96x96 pixels)
  use fewer convolution layers
     could degrade accuracy
accelerate convolution layer (matrix multiplication) with CGRA
  it will probably be necessary to add a flash memory to the CGRA as some of the layers are rather large and with the current setup it would create a large communication overhead
Notes: TF Lite File 300kB in size

## Slide 22
ROADMAP Manuca-FPGA SPI connection
Check if Manuca extension Board generates the expected SPI output
 DONE
1. Manuca: SPI Output
Write python script that converts the bit pattern received from MISO to hex pattern
1011 1111  xFD
 DONE
2. Bit to Hex pattern
Replace the PC and QSPI controller with the Manuca Board
establish the physical connection for SPI communication
 DONE
3.physical connection FPGA- Manuca
establish RD/WR via SPI connection between Manuca board and FPGA and check the correctness of the communication
 WIP, script done, still needs to be tested
4.RD/WR via SPI
Integrate the endian switch into the mbedOS code to make the python script superfluous
5. Integrate Endian into mbedOS

## Slide 23
Manuca-FPGA SPI connection